## Slide 1
Control/Branch Hazards

## Slide 2: Control/Branch Hazards
Caused by a delay in the availability of an instruction or the memory address needed to fetch the instruction
In ideal pipelined execution, a new instruction is fetched every cycle, while the previous instruction is being decoded
Instruction addresses are pre-determined, PC [PC]+4
However, branch instructions can alter this sequence
Branch instructions needs to finish execution first
  To determine whether and where to branch
Pipeline stalled before the branch outcome is known
C.2, 3.1 Pipeline hazards

## Slide 3: Conditional Branches – 1
Consider a conditional branch instruction such as
Testing the branch condition (comparing [x5] and [x6]) determines whether the branch is taken or not taken
  also, compute branch target address PC + loop
loop: ld f1, 0(x6)
...
BEQ x5, x6, loop
add x2, x4, x5
C.2, 3.1 Pipeline hazards
Notes: branch instruction execution: calculate target address, and resolve branch condition
define “taken” and “non taken”

## Slide 4: Conditional Branches – 2
Both comparison and target address calculation happen in EX stage (3rd cycle of instruction processing)
Stall penalty = 2 cycles
  Cannot fetch the branch target before the start of 4th cycle
  No useful instruction fetched in cycles 2 and 3
C.2, 3.1 Pipeline hazards

## Slide 5: Handling Control Hazards
If x5 = x6, in cycle-3, EX stage determines that the branch is taken and computes the target address
Two instructions ( and ) on the wrong path have already been fetched
C.2, 3.1 Pipeline hazards
time
BEQ x5, x6, loop

## Slide 6: Handling Control Hazards
Control transfers to branch target ‘loop’
Instructions and flushed from the pipeline
Branch Penalty in this case is 2 cycles
What would be the branch penalty if the branch was not taken?
C.2, 3.1 Pipeline hazards
j: BEQ x5, x6, loop

## Slide 7: Reduce Branch Penalty
Finish branches in ID stage
  Compute the branch target address in the ID stage
    Need an adder in the ID stage to add the branch offset to the PC
  Test the branch condition in the ID stage
    Move the comparator from EX stage to ID stage
    Branch condition tested in parallel with target address computation
  Update the PC before the end of ID stage
  Branch penalty reduced to one cycle
Negative Effect: higher ID stage delay; may have to increase the clock period
C.2, 3.1 Pipeline hazards

## Slide 8: Reduce Branch Penalty
Branch condition and target address computed in cycle # 2
Branch penalty reduced to one cycle
Only one instruction ( j+1 ) is fetched incorrectly and discarded
C.2, 3.1 Pipeline hazards
j: BEQ x5, x6, loop

## Slide 9: Reducing Branch Penalty – Branch Prediction
Predict-not-taken
  Increment PC by 4 every cycle and keep fetching sequential instructions after the branch instruction
  After the branch outcome is computed
    If the branch is actually Not-taken
      We have already been fetching instructions from the correct path => no problem
    But if the branch is actually Taken
      Need to start fetching from the branch target
      What happens to the instructions that have already been fetched on the wrong path?
C.2, 3.1 Pipeline hazards

## Slide 10: Reducing Branch Penalty
Predict-not-taken
C.2, 3.1 Pipeline hazards

## Slide 11: Reduce Branch Penalty – Branch Prediction
Predict-taken: assume every branch as taken
  In our 5-stage pipeline, we do not know branch target earlier than branch outcome
  No advantage, unless we could predict the target address earlier in the pipeline
Delayed Branch (not discussed further)
  Compiler optimization
  Use knowledge of the program semantics to rearrange instructions before/after the branch
  Useful for short pipeline – no longer used in RISC-V
C.2, 3.1 Pipeline hazards

## Slide 12: Delayed Branch
Branch instruction
Sequential successor - in branch delay slot
Branch target if taken
C.2, 3.1 Pipeline hazards

## Slide 13: Example
SD x7, 0(x8)
BEQ x5, x6, IF
LD x2, 16(x1)
DADD x3, x4, x2
IF: LD x2, 64(x1)
DSUB x3, x4, x2
Branch hazards?
Data hazards?
How much is branch penalty?
C.2, 3.1 Pipeline hazards
Notes: What instruction in the sequence can be move between BEQ and LD?
move SD as it is independent of the other instructions.

## Slide 14: Performance of Branch Schemes
C.2, 3.1 Pipeline hazards

## Slide 15: Performance of Branch Schemes - Example
Branches comprise 20% (BF) of all instructions. Branch prediction is 80% accurate (BPA). 2 cycle stalls (SP) on each mis-prediction. Compute average branch penalty control hazards on CPI of the pipelined processor.
CPI without control hazards = 1
Stall cycles = BF* (1 – BPA) * SP = 20% * (1 - 80%) * 2 = 0.08
CPI with branch penalty = 1 + 0.08 = 1.08
C.2, 3.1 Pipeline hazards

## Slide 16: Another Example
Speedup of “predicted-not-taken” over “stall pipeline” = 1.56 / 1.38 = 1.13
C.2, 3.1 Pipeline hazards
Notes: Starting question: what are approaches to handling branch hazards?
This example shows their benefits

## Slide 17: Branch Prediction
Static Prediction – high misprediction rate
  Prediction for branches is fixed at taken or not-taken
  Based on profile information
Dynamic Prediction
  Use runtime history of branches to predict outcome of current branch
  Better performance for various programs
  Higher HW complexity
C.2, 3.1 Pipeline hazards
Notes: Hypothesis: a branch (taken or not-taken) will likely repeat the same decision next time.
This is true for branches involved in loops. --- a type of temporal locality
Low order bits of branch instruction addresses are used to index Branch-prediction buffer (BPB)

## Slide 18: 1-Bit Predictor
  1 bit predictor - remember last taken/not taken per branch
  Use part of the PC (low-order bits) to index buffer/table – multiple branches may share the same bit
  Invert the bit if the prediction is wrong
Predict
Taken
Predict Not Taken
T
T
NT
T
NT
NT
Prediction
NT
T
T
T
NT
T
T
NT
NT
K-bit
Branch
address
2k
C.2, 3.1 Pipeline hazards
Notes: What about PCs of two branches having the same lower bits?

## Slide 19: Branch History Table (BHT)
Also called Branch Prediction Buffer (BPB)
Each entry implements 1-bit predictor – low accuracy
BHT indexed by bits from PC
  Similar to direct mapped cache
  More entries, more cost, but less conflicts, higher accuracy
Backward branches for loops will be mis-predicted twice
  Once upon loop exit and then again on loop entry
More complex predictors for better prediction
What about PCs of two branches having the same lower bits?
C.2, 3.1 Pipeline hazards

## Slide 20: 1-Bit Predictor
Consider a loop of 9 iterations before exit:
  First time through inner loop, predicts exit instead of looping
  End of inner loop, predict looping instead of exiting
  Mis-predict twice every time the inner loop is executed
C.2, 3.1 Pipeline hazards
  outer: for (…) {
  inner: for (i=0; i<9; i++)
  a[i] = a[i] * 2.0;
  }

## Slide 21: 2-Bit Predictor
Optimization: 2-bit scheme where change prediction only if get mis-prediction twice consecutively
Other solutions: correlating predictor, tournament predictors
C.2, 3.1 Pipeline hazards

## Slide 22: 2-Bit Predictor Accuracy
BHT: 4096 entry 2-bit buffer
C.2, 3.1 Pipeline hazards
FP programs
Integer
programs

## Slide 23: Impact of BHT Size
C.2, 3.1 Pipeline hazards
4K vs Unlimited Buffer for Prediction

## Slide 24: Correlating Branch Predictors
If (aa == 2)
aa = 0;
If (bb == 2)
bb = 0;
If (aa != bb) {…}
If both b1 and b2 are not taken, then b3 is taken.
Use history of last m branches to predict the current one.
3.3 Advanced Branch Prediction
addi x3, x1, –2
bnez x3, L1 // branch b1 (aa!=2)
add x1, x0, x0 //aa=0
L1: addi x3, x2, –2
bnez x3, L2 // branch b2 (bb!=2)
add x2, x0, x0 //bb=0
L2: sub x3, x1, x2 //x3=aa-bb
beqz x3, L3 // branch b3 (aa==bb)
Notes: branches are often correlated
branch b3 is correlated to b1 and b2.

## Slide 25: Correlating Branch Predictors
Use history of last m branches to predict the current branch.
  Each predictor uses n bits.
Global history register
of last m branches
t – taken
nt – not taken
Shift register
BHT
3.3 Advanced Branch Prediction
2m entries
n-bits
<-- n-bit -->
t | nt | t | t | nt
Notes: Benefit: higher prediction accuracy, low HW overhead.

## Slide 26: Correlating Branch Predictors
Use additional k-bits of branch instruction address for better correlation
Global history register
of last m branches
Shift register
Branch prediction buffer
(2m+k entries, each of n-bits)
Low order k-bits
of branch address
m+k
3.3 Advanced Branch Prediction
2m+k entries
n-bits
<-- n-bit -->
t | nt | t | t | nt
Notes: Using k-low order address bits of the current branch instruction to reduce interferences among different branch instructions.

## Slide 27: Tournament Predictors
Tournament predictor selects the best of local and global predictors, and leads to better prediction.
3.3 Advanced Branch Prediction

## Slide 28: Summary—Dependences & Hazards
Structural dependence, s-hazard
  Duplicate hardware
Data dependence, RAW/WAR/WAW hazards
  forwarding
  out-of-order execution -- to be discussed later
Control/branch dependence, branch hazard
  branch prediction
  hardware speculation – to be discussed later