## Slide 1
Suppose the following measurements
fraction of FP ops = 25%
Average CPI of FP ops = 4 cycles
fraction of FPSQR = 2%
Average CPI of FPSQR = 20 cycles
Average CPI of other inst = 1.33 cycles
Design #1: decrease CPI of FPSQR to 2
Design #2: decrease CPI of FP ops to 2.5
Compare these two design alternatives.
1.9 Quantitative Principles of Computer Design
Solution
Original CPI = (4 x 25%) + (1.33 x 75%) = 2.0
Design #1: New CPI = 2.0 – 2% ( 20 – 2) = 1.64
Design #2: New CPI = (75% x 1.33) + (25% x 2.5) = 1.625
Speedup = 2.00/1.625 = 1.23

## Slide 2
Find the number of dies per 300 mm (30 cm) wafer for a die
that is 1.5 cm on a side and for a die that is 1.0 cm on a side
1.9 Quantitative Principles of Computer Design
Solution

## Slide 3: Integrated Circuit: Wafer and Die
wafer
die
1.6 Trends in Cost

## Slide 4
Find the die yield for dies that are 1.5 cm on a side and 1.0 cm on a side, assuming a defect density of 0.047 per cm2 and N is 12
1.9 Quantitative Principles of Computer Design
Solution