## Slide 1
Pipeline Scheduling
Computer Architecture
A Quantitative Approach, Fifth Edition
Pipeline Scheduling

## Slide 2: Overview
Simple 5-stage pipeline is in-order execution
  instructions executed in program order
  dependences and hazards lead to many stall cycles
We will discuss a more advanced arch.: dynamic scheduling & out-of-order execution
  HW re-order instruction execution dynamically, and
  Ensure program semantics unchanged
  Significantly improve performance

## Slide 3: Objectives and Reading
Objectives
  Understand static and dynamic scheduling to exploiting ILP
  Understand the working of Tomasulo’s algorithm
Reading
  H&P book, Section 3.2, 3.4, 3.5

## Slide 4
Instruction-Level Parallelism – Review

## Slide 5: Instruction-Level Parallelism
Overlap executions of multiple instructions
When exploiting instruction-level parallelism, goal is to minimize CPI
  Effective CPI = Ideal pipeline CPI
        + stalls (structural, data, control hazards)
3.1 ILP Concepts and Challenges

## Slide 6: Data Dependencies
Dependencies are a property of programs
Pipeline determines if dependence is detected and if it causes a stall
Data dependency conveys:
  Possibility of a hazard
  Order in which results must be calculated
  Upper bound on exploitable instruction level parallelism
Dependencies that flow through memory locations are difficult to detect
      SD x1, 45(x5)
      LD x2, 90(x7) // possible that 45+[x5] == 90+[x7]
3.1 ILP Concepts and Challenges

## Slide 7: Name Dependence
Two instructions use the same name but no flow of information – not a true data dependence
  Anti-dependence: instruction j writes a register or memory location that instruction i reads
        add x2, x3, x4
        ld x3, 90(x7)
  Output dependence: instruction i and instruction j write the same register or memory location
        add x2, x3, x4,
        ld x2, 90(x7)
  To resolve name dependence, use renaming techniques
3.1 ILP Concepts and Challenges

## Slide 8: Data Hazards
A data hazard exists between two dependent instructions that are close in a program such that overlapping their executions would change the order of accesses to the operand involved in the dependence.
Data Hazards
  Read after write (RAW)
  Write after write (WAW)
  Write after read (WAR)
3.1 ILP Concepts and Challenges

## Slide 9: Overcome Hazards
1: addi x2, x3, 100
2: subi x9, x2, 30
3: or x4, x5, x6
Assume no forwarding
# stall cycles on 5-stage pipeline?
Notes: changes order of instruction while maintaining all dependences – to reduce CPI

## Slide 10: Control Dependences
Control Dependence determines ordering of instruction i with respect to a branch instruction
  Instruction control-dependent on a branch cannot be moved before the branch so that its execution is no longer controller by the branch
  An instruction not control-dependent on a branch cannot be moved after the branch so that its execution is controlled by the branch
s1
if p1 then
s2
s3
3.1 ILP Concepts and Challenges
Notes: scheduling often changes order of instructions, but such change cannot break control dependence

## Slide 11: Control Dependence – Examples
LD cannot be move above branch
OR instruction dependent on ADD and SUB
  Cannot move SUB before the branch
Reorder instruction if it does not change program semantics
Example 1:
ADD x2, x3, x4
BEQ x2, x0, L
LD x1, 0(x2)
L: …
Example 2:
ADD x1, x2, x3
BEQ x4, x0, L
SUB x1, x5, x6
L: ...
OR x7, x1, x8
3.1 ILP Concepts and Challenges
Notes: Case 1: if x2 = 0, moving LD before BEQ may cause memory access exception.
Case 2: OR reads X1, which may be updated by either ADD or sub.

## Slide 12: Control Dependence – Examples (1)
Reorder instruction if it does not change program semantics
Example 3: ok to move sub above BEQ
  if x4 is not used after label “skip”
3.1 ILP Concepts and Challenges
Example 3
ADD x1, x2, x3
BEQ x12, x0, skip
SUB x4, x5, x6
ADD x5, x4, x9
skip: OR x7, x8, x9

## Slide 13: Impacts of Dependences
Parallelism with basic block is limited
  Typical size of basic block = 3-6 instructions
  Must optimize across branches
Challenges: dependency
  Dependent instructions cannot be executed simultaneously or close to each other
Increase ILP – Loop-Level Parallelism
  Unroll loop statically or dynamically
3.1 ILP Concepts and Challenges
Notes: programs that take a lot of time usually contain large loops – optimizing ILP for loops is critical

## Slide 14
3.2 Compiler Techniques for Exposing ILP

## Slide 15: More Sophisticated Pipeline
fadd.d f3, f5, f6
stall stall stall A1 A2
Notes: If an instruction “fadd.d f3, f5, f6” is after the 3rd instruction, it is independent, but still has to wait for the previous fadd.d instruction to complete.
-- scheduling is to detect such instructions, and let them proceed without necessarily follow the program order

## Slide 16: Pipeline Scheduling
Separate dependent instruction from the source instruction by the pipeline latency
  Pipeline latency – cycles to separate two dependent instructions to avoid hazards
By inserting NOP (bubbles) – pipeline stalls (interlock)
By inserting independent instructions – Scheduling
  Statically, or Dynamically
Scheduling relies on
  ILP in programs
  latencies of functional units
3.2 Basic Compiler Techniques for Exposing ILP
Notes: Pipeline latency – number of cycles for the source instruction to produce data.

## Slide 17: Static Scheduling
Transform and re-arrange the code
  while maintaining all dependencies in program
Example:
3.2 Basic Compiler Techniques for Exposing ILP
  for (i=999; i>=0; i=i-1)
  x[i] = x[i] + s;

## Slide 18: Static Scheduling (1)
Loop: fld f0, 0(x1)
stall
fadd.d f4, f0, f2
stall
stall
fsd f4, 0(x1)
addi x1, x1, -8
bne x1, x2, Loop
3.2 Basic Compiler Techniques for Exposing ILP
Notes: Stall can be viewed as a special instruction that does not to the pipeline.

## Slide 19: Static Scheduling (2)
ILP in basic blocks is limited
Loop unrolling to increase ILP
Loop: fld f0, 0(x1)
addi x1, x1, -8
fadd.d f4, f0, f2
stall
stall
fsd f4, 8(x1)
bne x1, x2, Loop
3.2 Basic Compiler Techniques for Exposing ILP

## Slide 20: Loop Unrolling
Number of live registers increase vs. original loop
Avoid dependence
Increase ILP
Unroll by a factor of 4 (assume # elements is divisible by 4)
Run in 26 cycles without scheduling
6.5 cycle/iteration
Loop: fld f0, 0(x1)
fadd.d f4, f0, f2
fsd f4, 0(x1) //drop addi & bne
fld f6, -8(x1)
fadd.d f8, F6, f2
fsd f8, -8(x1) //drop addi & bne
fld f10, -16(x1)
fadd.d f12, f10, f2
fsd f12, -16(x1) //drop addi & bne
fld f14, -24(x1)
fadd.d f16, f14, f2
fsd f16, -24(x1)
addi x1, x1, -32
bne x1, x2, Loop
3.2 Basic Compiler Techniques for Exposing ILP
Notes: instructions in different iterations use different registers – high demand on free registers
Branch overhead instructions are 2 over 4 iterations in the unrolled loop, instead of 2 in each iteration in the original loop – saving some execution cycles

## Slide 21: Loop Unrolling/Pipeline Scheduling
After scheduling
No stalls
Run in 14 cycles
3.5 cycles/iteration
Loop: fld f0, 0(x1)
fld f6, −8(x1)
fld f10, −16(x1)
fld f14, −24(x1)
fadd.d f4, f0, f2
fadd.d f8, f6, f2
fadd.d f12, f10, f2
fadd.d f16, f14, f2
fsd f4, 0(x1)
fsd f8, −8(x1)
fsd f12, 16(x1)
fsd f16, 8(x1)
addi x1, x1, −32
bne x1, x2, Loop
3.2 Basic Compiler Techniques for Exposing ILP

## Slide 22: Loop Unrolling – Limitations
Code size increases as #iterations to unroll increases
Register shortfall
  instructions in different iterations are assigned with different register names to avoid conflict
Not able to identify independent instruction based on runtime information
Cross loop iteration dependence
  limits amount of ILP that can be exposed
3.2 Basic Compiler Techniques for Exposing ILP
      SD x1, 45(x5)
      LD x2, 90(x7)