## Slide 1
Pipelining – Basic Review
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 2: Objective and Reading
Objective
  Review of basic pipelining architecture – how it improves performance, and its issues
  Introduce ILP
Reading
  Appendix C.1
  Chapter 3.1

## Slide 3: A Simplified View of Computers
CPU
Interconnect
HD
DISP
KB
Memory
...
I$
D$

## Slide 4
C.1 Introduction
C.1 Introduction

## Slide 5: Introduction
Design Principle – exploit parallelism
Pipelining become universal technique in 1985
  Overlaps execution of instructions
  Exploits Instruction Level Parallelism (ILP)
Two main approaches to detect ILP
  Hardware-based dynamic approaches
    Used in server and desktop processors
    Not used as extensively in PMD processors
  Compiler-based static approaches
    Not as successful outside of scientific applications
C.1 Introduction
Fetch
Decode
Execute
Writeback

## Slide 6: Instruction Execution of RISC
Initial State: PC is set to point to the first instruction
For each instruction, perform the following 5 steps:
  Instruction Fetch (IF)
  Instruction Decode/Register Read (ID)
  Execution/Effective Address Calculation (EX)
  Memory Access (MEM)
  Write Back (WB)
C.1 Introduction
Notes: an instruction is executed in series of stages

## Slide 7: Instruction Execution
Instruction Fetch:
  Send PC to memory, assert MemRead signal
  Instruction fetched from memory
  Place instruction in IR: IR  Mem[PC]
  Update PC to next instruction: PC  [PC] + 4
C.1 Introduction
Notes: Why is IR needed? Allow memory access and instruction execution proceed in parallel

## Slide 8: Instruction Execution
Instruction Decode:
  Instruction in IR decoded by control logic, instruction type and operands determined
  Source operands read from general purpose register file, etc
C.1 Introduction
Notes: Actions:
read registers,
check equality on registers for branch instructions
compute branch target address
sign-extend immediate/displacement field
All actions performed in parallel -> higher performance, may lead to waster of energy if actions are not needed.

## Slide 9: Instruction Execution
Execute:
  ALU operates on operands prepared in previous cycle
  One of four functions depending upon opcode
  Memory Reference
    Form effective address from base register and immediate offset
    ALU Output  [A] + Imm
  Register-Register ALU Instruction
    ALU Output  [A] op [B]
  Register-Immediate ALU Instruction
    ALU Output  [A] op Imm
  Branch
    Compute branch target by adding Imm to PC
      ALU Output  [PC] + (Imm << 2)
    Evaluate the branch condition
C.1 Introduction

## Slide 10: Instruction Execution
Memory Access:
  For load instructions, read data from memory
  For store instructions, write data to memory
C.1 Introduction

## Slide 11: Instruction Execution
Write-back:
  Results written to destination register
  Results from mem read or ALU
C.1 Introduction

## Slide 12: Instruction Execution – Example
add X3, X4, X5 ; X3[X4]+[X5]
Source registers: X4, X5 Destination register: X3
Instruction steps:
  Fetch: Fetch the instruction into IR and increment the program counter
  Decode: Decode the instruction in IR to determine the operation to be performed (add). Read the contents of registers X4 and X5
  Execute: Compute the sum [X4] + [X5]
  Memory Access: No action, since there are no memory operands
  Write-back: Write the result into register X3
C.1 Introduction

## Slide 13: Instruction Execution – Example
ld X5, N(X7) ; X5[[X7]+N]
Source register: X7 Destination register: X5
Immediate value N is given in the instruction word
Instruction steps:
  Fetch: Fetch the instruction and increment the program counter
  Decode: Decode the instruction in IR to determine the operation to be performed (load). Read the contents of register X7
  Execute: Add the immediate value N to the contents of X7
  Memory Access: Use the sum N+[X7] as the effective address of the source operand, read the contents of that location from memory
  Write-back: Write the data received from memory into register X5
C.1 Introduction

## Slide 14: Instruction Execution – Example
sd X6, N(X8) ;Mem[N+[X8]][X6]
Source registers: X6, X8 Destination register: None
The immediate value N is given in the instruction word
Instruction steps:
  Fetch: Fetch the instruction and increment the program counter
  Decode: Decode the instruction in IR to determine the operation to be performed (store). Read the contents of registers X6 and X8.
  Execute: Compute the effective address N + [X8]
  Memory Access: Store the contents of register X6 into memory location N + [X8]
  Writeback: No action
C.1 Introduction

## Slide 15: Basic Pipeline
To improve performance, we can make circuit faster, or use …
C.1 Introduction

## Slide 16
Pipeline clock cycle determined by the slowest stage.
Pipeline registers add extra overhead.
C.1 Introduction
Notes: This simple version misses some key components.
Note: Reg is updated in the 1st half of ID cycle, and it is read in the 2nd half of the ID cycle. so the 1st and 4th instructions can proceed in the same cycle even with a data dependency.

## Slide 17: Ideal Pipeline Performance
Balanced pipeline (each stage has the same delay)
Ignore overhead due to clock skew and pipeline registers
Ignore pipeline fill and drain overheads
C.1 Introduction
Number of pipeline stages
Notes: Fill and Drain overhead becomes higher as a pipeline become deeper.
The number of pipeline stages gives upper limit of performance improvement by pipelining.

## Slide 18: Pipeline Performance
Example: A program consisting of 500 instructions is executed on a 5-stage processor. How many cycles would be required to complete the program. Assume ideal overlap in case of pipelining.
Without pipelining:
  Each instruction will require 5 cycles. There will be no overlap amongst successive instructions.
  Number of cycles = 500 * 5 = 2500
With pipelining:
  Each pipeline stage will process a different instruction every cycle. First instruction will complete in 5 cycles, then one instruction will complete in every cycle, due to ideal overlap.
  Number of cycles = 1*5 + (499*1) = 504
Speedup with pipelining = 2500/504 = 4.96
C.1 Introduction

## Slide 19: Pipeline Performance
Problem: Consider a non-pipelined processor using the 5-stage datapath with 1 ns clock cycle. Assume that due to clock skew and pipeline registers, pipelining the processor adds 0.2 ns of overhead to the clock cycle. How much speedup can we expect to gain from pipelining? Assume a balanced pipeline and ignore the pipeline fill and drain overheads. (A similar ex. in the book)
Solution:
  Without pipelining: Clock period = 1 ns, CPI = 5
  With pipelining: Clock period = 1 + 0.2 = 1.2 ns, CPI = 1
C.1 Introduction

## Slide 20: Pipeline Performance
The potential increase in performance resulting from pipelining is proportional to the number of pipeline stages
However, this increase would be achieved only if
  all pipeline stages require the same time to complete, and
  there is no interruption throughout program execution
Unfortunately, this is not true
  there are times when an instruction cannot proceed from one stage to the next in every clock cycle
C.1 Introduction

## Slide 21: Pipeline Performance – cont’d
Pipeline stages need to be balanced
  the clock is fixed by the slowest stage.
Ideally, every stage has same latency
In reality, stages are unbalanced
  memory accesses are much slower
Example: MEM has 10 ns latency, other stages have 2 ns latency
  clock cycle time = 10 ns
  Reducing memory latency is critical  memory hierarchy
Other factor: pipeline stalls

## Slide 22: Pipeline Stalls
Assume that Instruction Ij+1 is stalled in the decode stage for two extra cycles
This will cause Ij+2 to be stalled in the fetch stage, until Ij+1 proceeds
New instructions cannot enter the pipeline until Ij+2 proceeds past the fetch stage after cycle 5 => execution time increases by two cycles
C.1 Introduction
Ij
Ij+1
Ij+2
Notes: Stalls are due to dependencies among instructions – cycles wasted

## Slide 23: Summary
Instruction executes in a sequence of stages
Multiple instructions can execute at the same time in different stages
  Instruction-level parallelism (ILP)
Pipelining architecture exploits ILP
Ideal pipelining performance improvement == # of pipeline stages
In reality, it suffers due to hazards
  More discussions on it are scheduled