## Slide 1: Memory Hierarchy Design

## Slide 2: Recall Pipeline Performance
Pipeline stages need to be balanced
  the clock is fixed by the slowest stage.
Ideal case, every stage has same latency
In reality, stages are unbalanced
  memory accesses are much slower
Example: MEM 10 ns latency, other stages 2 ns latency
  clock cycle time = 10 ns
How do reduce MEM stage latency?
  Memory hierarchy

## Slide 3: A Simplified View of Computers
CPU
Interconnect
HD
DISP
KB
Main Memory
...
I$
D$
Memory
Notes: Logically, memory viewed a mono block
Practically, memory organized with layers of different types of memory: SRAM for cache, DRAM for main memory, non-volatile memory (HD/Flash)

## Slide 4: Objectives and Reading
Objectives
  Understand memory hierarchy organizations and their impacts on performance
  Evaluate performance tradeoffs of different memory hierarchy organizations
Reading
  Computer Architecture: A Quantitative Approach
    Appendix B, Chapter 2
  Computer Organization and Design: The Hardware/Software Interface
    Chapter 5

## Slide 5: Memory Technology – Overview
Static RAM (SRAM)
  0.5ns – 2ns, $2000 – $5000 per GB
Dynamic RAM (DRAM)
  20ns – 30ns, $10 – $50 per GB
Flash – non-volatile
  20 – 100 us, 5-10x cheaper than DRAM
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB
Ideal memory
  Access time of SRAM,
  Capacity and cost/GB of disk
slower, cheaper
faster, costlier
Notes: Flash memory is 1000x slower than DRAM, 1000x faster than HD

## Slide 6: The “Memory Wall” Problem
Processor mem accesses/sec vs DRAM accesses/sec

## Slide 7: Computer Energy Usage
Notes: What principles can we derive from this and previous slides?

## Slide 8: The “Memory Wall” – A Multi-Core Case
Aggregate peak bandwidth grows with # cores:
  Intel Core i7 can generate two references per core per clock
  Four cores and 3.2 GHz clock
    25.6 billion 64-bit data references/second +
    12.8 billion 128-bit instruction references/second
    = 409.6 GB/sec
DRAM bandwidth is only 6% of this (25 GB/s)
How does memory meet processor bandwidth demand?
      Multi-port, pipelined caches
      Two levels of cache per core
      Shared third-level cache on chip
2.1 Introduction

## Slide 9: Principle of Locality – Review
Temporal locality
  Programs often access a small proportion of their address space at any time
  Items accessed recently are likely to be accessed again soon
  e.g., instructions and variables in a loop
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data
B.1 Introduction
Notes: locality is a property of applications

## Slide 10: Principle of Locality – Review
Identify Temporal and spatial locality
int sum = 0;
int x[1000];
for (int c = 0; c < 1000; c++) {
sum += x[c];
x[c] = 0;
}
B.1 Introduction

## Slide 11: Memory Hierarchy – Basic Idea
Ideally memory = unlimited capacity with low latency
Fast memory technology is more expensive per bit than slower memory
Solution: organize memory system into a hierarchy
  Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Temporal and spatial locality ensures that nearly all references can be found in smaller memories
  Gives the illusion of a large, fast memory being presented to the processor
2.1 Introduction
Notes: locality: majority of memory accesses in a small space.

## Slide 12: Memory Hierarchies
2.1 Introduction
Mobile devices
Desktop
Servers
Notes: requirements of different applications  different mem hierarchy designs

## Slide 13: Energy Consumptions
Song Han, FPGA’17 talk, “Deep Learning – Tutorial and Recent Trends”
2.1 Introduction
More cache accesses lead to better efficiency