## Slide 1
Basic Cache Organizations

## Slide 2: Memory Hierarchy Questions
Data transferred between cache & memory are in blocks
Block placement - where can a block be placed in the upper level?
Block identification – how to find a block in the upper level?
Block replacement - which block should be replaced on a miss?
Write strategy – how to handle writes?
B.1 Introduction

## Slide 3: Basics
When a word is found in cache --> cache hit.
When a word is not found in the cache, a miss occurs:
  Fetch word from lower level in hierarchy does not reduce latency
  Lower level may be another cache or the main memory
  Also fetch the other words contained within the block
    Takes advantage of spatial locality
  Place block into cache in any location within its set, determined by address
CPU
Cache
Main
Memory
word
block
B.1 Introduction
Notes: Why do we fetch a block instead of a single word?

## Slide 4: Basics
Inclusive cache (considered for this class)
Exclusive cache
CPU
L1$
L2$
CPU
L1$
L2$
B.1 Introduction
Notes: Inclusive -- miss penalty is less
Exclusive – higher miss penalty, less memory waste
Exclusive cache might not work well in multiprocessor as requested data only exists in a remote cache  longer access latency

## Slide 5: Direct Mapped Cache
Only one choice
cache index = (Block address) MOD (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits to access bytes in a block
B.1 Introduction
Notes: Q: what are block address and block offset used for?

## Slide 6: Tags and Valid Bits
One cache line  Multiple memory blocks
  Cache line is aka cache block
How do we know which particular memory block is stored in a cache location?
  For write, store tag bits as well as the data
  For read, match tags in addressed and that stored in $
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0
B.1 Introduction

## Slide 7: Example: Larger Block Size
Cache: 64 blocks, 16 bytes/block
  To what cache block number does address 1200 (decimal) map?
  Assume 32-bit address
  Byte-addressable
B.1 Introduction
V
tag
block 0
V
tag
block 1
V
tag
block 63
…
32
address

## Slide 8: Example: Larger Block Size
Cache: 64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block offset value = 1200 modulo 16 = 0
Cache block index = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
B.1 Introduction

## Slide 9: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 0 |  | 
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 0 |  | 
111 | 0 |  | 
B.1 Introduction
Gray area is what’s actually included in cache

## Slide 10: Cache Example
Index | V | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 0 |  | 
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110
B.1 Introduction
1
compulsory
miss

## Slide 11: Cache Example
Index | V | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 1 | 11 | Mem[11010]
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010
B.1 Introduction
2

## Slide 12: Cache Example
Index | V | Tag | Data
000 | 1 | 10 | Mem[10000]
001 | 0 |  | 
010 | 1 | 11 | Mem[11010]
011 | 1 | 00 | Mem[00011]
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000
B.1 Introduction
3
4
5

## Slide 13: Cache Example
Index | V | Tag | Data
000 | 1 | 10 | Mem[10000]
001 | 0 |  | 
010 | 1 | 10 | Mem[10010]
011 | 1 | 00 | Mem[00011]
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010
B.1 Introduction

## Slide 14: Address Subdivision
B.1 Introduction
 from CPU
1
2
3
Notes: Operations for cache hit and miss

## Slide 15: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU
  Fetch a block from next level of mem. hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access
B.1 Introduction
Notes: Note that speculative and multithreaded processors may execute other instructions during a miss
  Reduces performance impact of misses

## Slide 16: Cache Misses
Miss rate
  Fraction of cache access that result in a miss
Miss Penalty – time to access lower level memory
Causes of misses
  Compulsory
    First reference to a block
  Capacity
    Blocks discarded and later retrieved due to cache capacity limit
  Conflict
    Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache
    Only happen in direct-mapped or set associative caches
2.1 Introduction

## Slide 17: Measuring Cache Performance
CPU time = (CPU cycles + mem stall cycles) * cycle time
  CPU cycles = IC*Ideal CPI (CPU cycles under cache hits)
  Memory stall cycles = additional cycles for handling cache misses
Stall cycles per instruction
B.1 Introduction
latency of accessing lower-level memory
Notes: CPU cycles = IC * Ideal CPI
CPU time = IC *(hit cycles + mem access/inst * miss rate * miss penalty) * cycle time

## Slide 18: Cache Performance – Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2 cycles (aka ideal CPI)
  Load & stores are 36% of instructions
Stall cycles per instruction
  I-cache: 1 × 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster
B.1 Introduction
Notes: What about performance if there is no cache?

## Slide 19: Cache Performance - Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
Example
  CPU with 1ns clock cycle time, hit time = 2 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 2 + 0.05 × 20 = 3 cycles
B.2 Cache Performance
AMAT = Hit time + Miss rate × Miss penalty
Notes: Time here can be clock cycles or physical time.
Question: why not AMAT = hit time * (1-Miss rate) + Miss rate * Miss penalty?

## Slide 20: Performance Summary
As CPU performance increased
  Miss penalty becomes more significant
Increasing clock rate, and decreasing base CPI
  Memory stalls lead to more CPU cycles
  Greater proportion of time spent on memory stalls
Cannot neglect cache behavior when evaluating system performance
  What does Amdahl’s law tell us?
B.2 Cache Performance
How to reduce memory stalls?

## Slide 21: Associative Caches – Reduce Conflict Misses
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry – expensive (area)
n-way set associative
  Each set contains n entries
  Block address determines the set
    Cache index = (Block address) MOD (#Sets in cache)
  Search all entries in a given set at once for correct one
  n comparators (less expensive than fully associative)
  Direct-mapped = 1-way associative
B.1 Introduction

## Slide 22: Associative Cache Example
B.1 Introduction
Fully Associative
Direct Mapped
2-way Associative

## Slide 23: 4-way Associative Cache Organization
1
2
3
Notes: A cache index points to a set, which includes a number of cache blocks.

## Slide 24: Associativity Example
Compare 4-block caches, block size = 1 byte
  Direct mapped, 2-way set associative, fully associative
  Sequence of addresses: 0, 8, 0, 6, 8
Direct mapped
Mem[0]
5 misses (their types?)
B.1 Introduction
0
1
2
3
Address 0
Mem[8]
Address 8
Mem[0]
Address 0
Mem[0]
Mem[6]
Address 6
Mem[8]
Mem[6]
Address 8
Notes: What types of misses can be found from the table?

## Slide 25: Associativity Example
2-way set associative
B.1 Introduction
Mem[0]
0
1
Address 0
Address 8
Address 0
Address 6
Address 8
Mem[0]
Mem[8]
Mem[0]
Mem[8]
Mem[0]
Mem[6]
Mem[8]
Mem[6]

## Slide 26: Associativity Example
Fully associative
B.1 Introduction
Mem[0]
Address 0
Address 8
Address 0
Address 6
Address 8
Mem[0]
Mem[8]
Mem[0]
Mem[8]
Mem[0]
Mem[8]
Mem[6]
Mem[0]
Mem[8]
Mem[6]

## Slide 27: Spectrum of Associativity
For a cache with 8 entries
B.1 Introduction
Notes: Given a fixed sized cache, increasing associativity  decreasing number of sets, and block address bits, increasing tag bits
Increasing tag bits  longer latency to compare

## Slide 28: Size of Tags vs Associativity
No. address bits = 32
Block size = 4 bytes
Cache size = 16KB 
Direct mapping
  Tag bits = 18x212
  Comparators = 1
4-way set-associative
  Tag bits= 4x210x20 = 20x212
  Comparators = 4
Fully associative
  Tag bits = 30x212
  Comparators = 212
1 0
13 2
31 14
1 0
11 2
31 12
1 0
31 2
B.1 Introduction
18 bits
20 bits
30 bits
Notes: As the associativity increases, the number of tag bits stored in cache also increases
 large circuit overhead,
 longer latency,
 higher energy consumption.

## Slide 29: Size of Tags vs Associativity
Increasing associativity requires
  More tag bits per cache block
  More comparators, each of which is more complex
    higher hit time, larger circuits
The choice among direct, set-associative and fully-associative mapping in any memory hierarchy will depend on
  Miss rate vs cost of implementing associativity, both in time and in extra hardware overhead
B.1 Introduction
AMAT = Hit time + (Miss rate) × Miss penalty

## Slide 30: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard otherwise
    FIFO approximates LRU – replace the oldest block
Random
  Gives approximately the same performance as LRU for high associativity
B.1 Introduction
Notes: Replacement policy is about conflict or capacity misses

## Slide 31: Write Policy – Write-Through
Update cache and memory together
  Cache and memory data remain the same
Easier to implement
Writes take longer – wait for mem update to complete
  e.g., if base CPI = 1, 10% of instructions are stores, memory write latency is 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
B.1 Introduction
CPU
Memory
Cache

## Slide 32: Write-Through with Write Buffer
Write buffer – holds data waiting to be written to memory
CPU write to cache & write buffer
Then, CPU continues immediately
Only stalls on write if write buffer is full
  Evict write buffer to memory
Write buffer is freed when write-to-memory is finished
B.1 Introduction
CPU
Memory
WBuf
Cache

## Slide 33: Write Policy – Write-Back
Just update the block in cache
  Keep track of whether each block is dirty - dirty bits
  Inconsistent data in $ and Mem
When a dirty block is replaced, write it back to memory
Write speed is faster
  One low-level memory update for multiple cache writes.
  Energy saving.
Write buffer can also be used
B.1 Introduction
CPU
Memory
Cache

## Slide 34: Write Allocation
What should happen on a write miss?
  Write allocate
  No-write allocate
Alternatives for write-through
  Write-allocate: fetch the block, then write-through
  No-write allocate: update memory w/o fetching the block
For write-back
  Usually fetch the block – write-allocate
  Act like read misses
B.1 Introduction
Notes: No-write allocate: aka write-around

## Slide 35: Write Miss Policies – Example
Assume fully associative cache
Find number of misses for the following write policies
  Write-through cache with No-write allocate
  Write-back cache with Write allocate
B.1 Introduction
write M[100]
write M[100]
read M[200]
write M[200]
write M[100]

## Slide 36: Handling Writes
 | Allocate | Non-Allocate
Write-Back | Allocate on write miss flush dirty blocks only when replaced write on hit only accesses cache | Write to mem on miss no cache block fetch
Write-Through | Allocate on write miss Write to cache & mem in parallel | Write to mem on miss no cache block fetch

## Slide 37: Cache Performance – Example
Base CPI = 1,
cycle time = 1ns
Hit time(DM) = 1 cycle
Miss rate (DM) = 0.021
Hit time (2-way) = 1.35 cycles
Miss rate (2-way) = 0.019
Miss penalty = 150 cycles
Avg mem. req/inst = 1.4
Which cache is faster using AMAT?
B.1 Introduction
Notes: amat is an indirect measure of system performance.
A better measure is CPU time considering memory stall cycles due to cache misses.

## Slide 38: Cache Performance – Example
Base CPI = 1,
cycle time = 1ns
Hit time(DM) = 1 cycle
Miss rate (DM) = 0.021
Hit time (2-way) = 1.35 cycles
Miss rate (2-way) = 0.019
Miss penalty = 150 cycles
Avg mem. req/inst = 1.4
Which cache is faster using CPU time?
B.1 Introduction
Notes: amat is an indirect measure of system performance.
A better measure is CPU time considering memory stall cycles due to cache misses.

## Slide 39: Cache Performance – Exercise
Base CPI = 1,
cycle time = 1ns
Hit time(DM) = 1 cycle
Miss rate (DM) = 0.021
Hit time (2-way) = 1.35 cycles
Miss rate (2-way) = 0.019
Miss penalty = 200 cycles
Avg mem. req/inst = 1.4
Which cache is faster?
B.1 Introduction
Notes: amat is an indirect measure of system performance.
A better measure is CPU time considering memory stall cycles due to cache misses.