## Slide 1
Basic Cache Optimizations

## Slide 2: Cache Performance – Review
Any optimization should consider its impact on all three factors
Hit time – often determines clock cycle time
Miss time – impact on pipeline stalls
  Miss rate
  Miss penalty
B.1 Introduction
AMAT = Hit time + Miss rate × Miss penalty
miss time
Notes: optimizing one parameter often has conflicting effects on the others.

## Slide 3: Six Basic Cache Optimizations
Larger block size
  Reduces compulsory misses
  Increases capacity and conflict misses, increases miss penalty
Larger total cache capacity to reduce miss rate
  Increases hit time, increases power consumption
Higher associativity
  Reduces conflict misses
  Increases hit time, increases power consumption
Multi-level cache to reduce miss penalty
  Reduces overall memory access time
Giving priority to read misses over writes
  Reduces miss penalty
Avoiding address translation in cache indexing
  Reduces hit time
B.3 Six Basic Cache Optimizations

## Slide 4: Optimization 1 – Larger Block Size
Reduce compulsory misses due to spatial locality
May increase conflict/capacity misses
Increase miss penalty
cache size
B.3 Six Basic Cache Optimizations
CPU
Memory
Cache

## Slide 5: Optimization 1 – Larger Block Size
Reduce compulsory misses due to spatial locality
May increase conflict/capacity misses
Increase miss penalty
AMAT
B.3 Six Basic Cache Optimizations
Notes: miss penalty depend on low-level mem.
high-latency high-BW -> larger block size

## Slide 6: Optimization 1 – Block Size Selection
Determined by lower level memory
High latency and high bandwidth – larger block size
Low latency and low bandwidth – smaller block size
B.3 Six Basic Cache Optimizations
CPU
Memory
Cache
bus bandwidth
Mem bandwidth
bandwidth = Bytes/s

## Slide 7: Optimization 2 – Larger Cache
Reduce capacity misses
Increases hit time
Increases power consumption
B.3 Six Basic Cache Optimizations

## Slide 8: Optimization 3 – Higher Associativity
Reduces conflict misses
Increases hit time
Increases power consumption
AMAT
B.3 Six Basic Cache Optimizations
Notes: 8-way works effectively as fully associative!

## Slide 9: Optimization 3 – Higher Associativity
Higher Associativity --> higher hit time
Larger miss penalty rewards higher associativity
Example:
Assume 4KB cache
AMAT(1-way) = 1 + 0.025 * miss penalty
AMAT(2-way) = 1.36 + 0.016 * miss penalty
Consider
1. miss penalty = 25 cycles
2. miss penalty = 100 cycles
B.3 Six Basic Cache Optimizations
Notes: Case 1: amat_1w = 1.625, amat_2w = 1.36 + 0.4 = 1.76
Case 2: amat_1w = 3.5, amat_2w = 1.36 + 1.6 = 2.96

## Slide 10: Optimization 4 – Multilevel Cache
L1 cache: small to keep hit time fast
L2 cache: capture as many L1 misses & reduce miss penalty for L1$
Local miss rates: miss rates of L1, L2
Global miss rates = miss rate(L1) * miss rate(L2)
B.3 Six Basic Cache Optimizations
CPU
Memory
L1$
L2$
1-2 cycles
20-30 cycles
~200 cycles
Notes: Simultaneously optimize hit time and miss time (miss rate x miss penalty)

## Slide 11: Optimization 4 – Multilevel Cache
HT: hit time
MR: miss rate
MP: miss penalty
AMAT = HT(L1) + MR(L1) * MP(L1)
MP(L1) = HT(L2) + LMR(L2) * MP(L2)
Mem Stall cycles/inst = misses/inst(L1) * HT(L2) + misses/inst(L2) *MP(L2)
misses/inst(L1) = M Accesses/inst * MR(L1)
misses/inst(L2) = M Accesses/inst * GMR(L2)
B.3 Six Basic Cache Optimizations
CPU
Memory
L1$
L2$
1-2 cycles
20-30 cycles
~200 cycles
global miss rate
Notes: Simultaneously optimize hit time and miss time (miss rate x miss penalty)
MP(L1) = AMAT(L2)

## Slide 12: Optimization 4 – Multilevel Cache
B.3 Six Basic Cache Optimizations
Among 1000 mem accesses, L1 misses = 40, L2 misses = 20
Q1: Local/global miss rates?
HT(L1) = 1 cycle
HT(L2) = 10 cycles
MP(L2) = 200 cycles,
Avg M Access/inst = 1.5
Q2: AMAT?
Q3: Avg stall cycles/inst?
Notes: Local miss rates: L1 = 0.04, L2 = 0.5
Global miss rates: L1 = 0.04, L2 = 0.02
AMAT = 1 + 0.04*(10 + 0.5*200) = 1 + 0.04*110 = 5.4 cycles
Average stall cycles/M-access: 4.4 cycles
Avg stall cycles/inst = avg mem/inst * Average stall cycles/M-access
= 1.5*4.4
= 6.6 cycles

## Slide 13: Optimization 4 – Multilevel Cache
L1 hit time affects CPU speed
  Prefers small and fast L1
Performance of L2 affects L1 miss penalty
  Prefers large L2 with higher associativity
  A little reduction in miss rate  big impacts on L2 speed due to large L2 miss penalty
See example in the book for the impact of higher associativity on miss rates/AMAT
B.3 Six Basic Cache Optimizations

## Slide 14: Optimization 4 – Multilevel Cache
Impact of L2 cache size on execution speed
B.3 Six Basic Cache Optimizations
Base line: 8192KB L2 cache with 1 cycle hit time
Notes: Base line: 8192KB L2 cache with 1 cycle hit time

## Slide 15: Optimization 5 – Giving Priority to Read Misses over Writes
Reduce miss penalty. See example below.
Write-through cache with write buffers suffers from RAW conflicts with main memory reads on cache misses:
  Write buffer holds updated data needed for the read.
  Alt #1 – wait for the write buffer to empty, increasing read miss penalty (in old MIPS 1000 by 50% ).
  Alt #2 – Check write buffer contents before a read; if no conflicts, let the memory read go first.
B.3 Six Basic Cache Optimizations
Notes: . Mem read accesses happen more frequent than writes.
. Amdahl law says we should focus on optimizing common cases.

## Slide 16: Optimization 5 – Giving Priority to Read Misses over Writes
Reduce miss penalty. See example below.
In a write-back cache, suppose a read miss causes a dirty block to be replaced
  Alt #1 – write the dirty block to memory first, then read memory.
  Alt #2 – copy the dirty block to a write buffer, read the new block, then write the dirty to memory.
B.3 Six Basic Cache Optimizations

## Slide 17: Optimization 6 – Avoid Address Translation during Cache Indexing to Reduce Hit Time
CPU
Cache
Memory
word
block
Hard Disk
page
B.3 Six Basic Cache Optimizations
Virtual Address
Physical Address
Notes: when processor runs, programs or data that it requests may be in memory or hard disk.
. From CPU’s view, virtual memory is as large as HD, and as fast as cache.
. Virtual address is translated to physical address before accessing the memory

## Slide 18: Optimization 6 – Avoid Address Translation during Cache Indexing to Reduce Hit Time
CPU
TLB
Cache
Mem
Conventional organization
Virtual address
(VA)
Physical Address
(PA)
PA
CPU
Cache
TLB
Mem
VA
VA
PA
Virtually addressed cache
CPU
TLB
L2 Cache
Mem
VA
PA
PA
L1 Cache
Tag
Virtually addressed physically tagged
page
offset
=
B.3 Six Basic Cache Optimizations
Hit?
Notes: virtual addressed caches lead to a number of complications as explained in the book.

## Slide 19: Optimization 6 – Avoid Address Translation during Cache Indexing to Reduce Hit Time
Cache size limited by the page size.
Increase size by higher associativity.
B.3 Six Basic Cache Optimizations