## Slide 1
Advanced Cache Optimizations

## Slide 2: Basic Ideas
Reduce hit time, miss rate, and miss penalty
  We have seen some optimizations
Increase cache bandwidth
  Bandwidth improves faster than latency
Reduce miss rate/penalty via parallelism
  Exploit parallelism
2.3 Advanced Cache Optimizations

## Slide 3: Opt 1 – Small and Simple L1 Caches
Critical timing path in cache hit:
  addressing tag memory, then
  comparing tags, then
  selecting correct block
Direct-mapped caches can overlap tag comparison and transmission of data
Lower associativity reduces power because fewer cache lines are accessed.
Higher associativity
  Increases size of virtually indexed cache
  Reduces conflict misses due to multithreading
2.3 Advanced Cache Optimizations

## Slide 4: Opt 1 – L1 Size and Associativity
Access time increases as size & associativity increases
As size increases, associativity other than 8 leads to smaller differences in access time.
2.3 Advanced Cache Optimizations

## Slide 5: Opt 1 – L1 Size and Associativity
Energy per read increases as size & associativity increases
2.3 Advanced Cache Optimizations
Notes: - Increase associativity -> higher energy consumption
- Avoid 8-way associativity cache due to large jump in energy consumption
+ Higher associativity needed for larger L1 cache if virtually indexed physical tagger cache is used to avoid translation.
+ higher associativity -> reduced miss rate for multithreading

## Slide 6: Opt 2 – Way Prediction
Way prediction set them before tag comparison is done.
2.3 Advanced Cache Optimizations
Tags
Data
1
2
3

## Slide 7: Opt 2 – Way Prediction
data
<<
=
=
=
=
offset
tag
2-bit index
2-bit
2-bit
Way Predictor
=
match
2.3 Advanced Cache Optimizations
if mis-match, the prediction is wrong
1
2
2
3

## Slide 8: Opt 2 – Way Prediction
Low order tag bits  prediction
  Predicts the next block to be accessed – what locality?
  Multiplexer could be set early to select the predicted block, only a single tag comparison
  A mis-prediction results in checking the other blocks
Prediction accuracy could be:
  > 90% for two-way
  > 80% for four-way
  I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
Extend to decide which block to access using way selection
  Intends to save power consumption.
  Increases mis-prediction penalty
2.3 Advanced Cache Optimizations
Notes: way prediction exploits both types of localities

## Slide 9: Opt 2 – Way Prediction
Performance evaluation
  HT1 : hit time when prediction is good
  HT2 : hit time when prediction is wrong
  MR : miss rate
  MP : miss penalty
  X : prediction accuracy
2.3 Advanced Cache Optimizations
Notes: Alternative: HT1*X + (1-X)(t + MR*MP) # t: extra time to handle mis-prediction.

## Slide 10: Opt 2 – Way Prediction Example
Miss rate = 0.1,
Miss penalty = 50 ns
HT = 3 ns without way prediction
HT1 = 2.5 ns when prediction is good
HT2 = 3.5 ns when prediction is wrong
Prediction accuracy X = 0.8
==============================================
AMAT_nw = 3 + 0.1*50 = 8 ns (no way prediction)
AMAT_W = (2.5*0.8 + 3.5*0.2) + 0.1*50 = 7.7 ns
Speedup = 8/7.7 = 1.05
Speedup on HT = 3/2.7 = 1.15
2.3 Advanced Cache Optimizations

## Slide 11: Opt 3 – Pipelining Cache
Increase bandwidth
Pipeline cache access to improve bandwidth
  Trend: shorter clock cycle, but hit time relative stable
    Cache hit handled in multiple cycles
  Examples – hit time in cycles
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Makes it easier to increase associativity
  In associative cache, tag compare and data output are serialized
Increases branch mis-prediction penalty
  Cache pipeline needs to be flushed in case of mis-prediction
2.3 Advanced Cache Optimizations

## Slide 12: Opt 3 – Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Interleave banks according to block address
  Mapping to banks: bank index = block address mod #banks
Figure 2.10 Four-way interleaved cache banks using block addressing. Assuming 64 bytes per block, each of these addresses would be multiplied by 64 to get byte addressing.
2.3 Advanced Cache Optimizations
Notes: bank # = index mod #banks eg. index = 10, #banks = 4, so bank # = 10 mod 4 = 2.

## Slide 13: Opt 4 – Nonblocking Caches
Allow data cache to service hits during a miss
  Reduces effective miss penalty
  “Hit under miss”
  Extended to “Hit under multiple miss”
  L2 often support this
2.3 Advanced Cache Optimizations
better
Notes: Evaluation of CPU performance becomes more complicated as the miss penalty is harder to compute for individual misses as misses and hits can overlap.
It also depends on the number of instructions CPU can execute before it must stall waiting for a previous miss to resolve.

## Slide 14: Opt 5 – Critical Word First, Early Restart
Processor needs one word in a block
Critical word first
  Request missed word from memory first
  Send it to the processor as soon as it arrives
Early restart
  Fetch the block in normal order
  Send missed word to the processor as soon as it arrives
Effectiveness of these strategies depends on block size and likelihood of another access to the portion of the block that has not yet been fetched
  More benefits if block size is larger
2.3 Advanced Cache Optimizations
Notes: what cache performance factor does it optimize?

## Slide 15: Opt 6 – Merging Write Buffer
When storing to a block that is already pending in the write buffer, update write buffer
Reduces stalls due to full write buffer
Do not apply to I/O addresses
w/o write merging
w write merging
2.3 Advanced Cache Optimizations
Notes: Benefits of write-merging:
Wr-buffer can hold more writes – more efficient use of buffer space
reduce number of writes to lower-level – less time to write

## Slide 16: Opt 7 – Compiler Optimizations
Gap between CPU and memory requires SW developer to look at memory hierarchy
/* before */
for (j=0; j < 16; j++)
for (i=0; i < 16; i++)
x[i][j] = 2*x[i][j];
2.3 Advanced Cache Optimizations
0 | x[0][0]
1 | x[0][1]
... | …
15 | x[0][15]
16 | x[1][0]
… | …
Notes: Increasing perf. gap between proc. and mem requires SW developers to pay attention to mem hierarchy

## Slide 17: Opt 7 – Compiler Optimizations
Loop Interchange
  Swap nested loops to access memory in sequential order
  Expose spatial locality
/* after*/
for (i=0; i < 16; i++)
for (j=0; j < 16; j++)
x[i][j] = 2*x[i][j];
2.3 Advanced Cache Optimizations
0 | x[0][0]
1 | x[0][1]
... | …
15 | x[0][15]
16 | x[1][0]
… | …
Notes: Increasing perf. gap between proc. and mem requires SW developers to pay attention to mem hierarchy

## Slide 18: Opt 7 – Compiler Optimizations
Blocking
  Instead of accessing entire rows or columns, subdivide matrices into blocks
  Requires more memory accesses but improves temporal locality of accesses
  See the book for an example
2.3 Advanced Cache Optimizations
Notes: Increasing perf. gap between proc. and mem requires SW developers to pay attention to mem hierarchy

## Slide 19: Opt 8 – Hardware Prefetching
Fetch two blocks on miss (include next sequential block)
Can hurt power if prefetched data are not used.
Some results obtained on Pentium 4 w. Pre-fetching
2.3 Advanced Cache Optimizations
better
Notes: prefetched blocks are placed in stream buffer.
Prefetching improves performance by reducing miss penalty

## Slide 20: Cache - Summary
A small and fast buffer between CPU and main memory
Direct mapped cache
  shorter hit time, higher miss rate, lower power consumption
Associative cache
  longer hit time, lower miss rate, higher power consumption
Performance evaluation
  AMAT – average memory access time: maybe misleading
  CPI with stall cycles due to cache misses: more accurate
  Various optimization to improve performance
2.3 Advanced Cache Optimizations

## Slide 22: Example: Intel Core I7 Cache
L1 I$ - 32 KB, L1 D$ - 32KB 8-way set associative, private
L2 – 256 KB, 8-way set associative, private
L3 – 8 MB, 16-way set associative, shared
L2
Notes: Pentium 4: 512 KB L2 cache, no L3.
High associativity in i7 is for multithreading, also pipelined cache reduces impact of high associativity