## Slide 1
Virtual Memory

## Slide 2: A Simple View of Memory Hierarchy
CPU
Cache
Memory
word
block
Hard Disk
page
B.3 Six Basic Cache Optimizations
Notes: when processor runs, programs or data that it requests may be in memory or hard disk.

## Slide 3: Why Virtual Memory
Limited physical memory leads to complications
  Size of a program is larger than main memory size
  Memory demand of multiple programs is larger than main memory size
Observation: a program often needs to small part of memory during its execution
  Load what is needed into main memory!
B.4 Virtual Memory
Notes: IBM PC at 1980s only came with 64KB main memory.

## Slide 4: Why Virtual Memory
Programs were divided into pieces and identified pieces that are mutually exclusive
These pieces were loaded and unloaded under user program control during execution
Calls between procedures in different modules lead to overlaying of one module with the other
Used to be done by hand
  Significant burden on programmers
B.4 Virtual Memory
Notes: Each program has its own virtual memory space.
Virtual M space is divided into blocks,
VM blocks are loaded if they are needed.
Fast program startup as not all blocks are loaded before exec.

## Slide 5: Basics of Virtual Memory
Programs use virtual addresses (VA)
Memory uses physical addresses (PA)
VA  PA at the page granularity
  pages can be anywhere in physical memory
  or in disk
Disk
…
OS
…
App1
…
App2
B.4 Virtual Memory

## Slide 6: Basics of Virtual Memory
Use physical DRAM as cache for disk
  Address space of a process can exceed physical memory size
  Sum of address spaces of multiple processes can exceed physical memory
Simplify memory management
  Multiple processes resident in main memory
    Each process with its own address space
  Only “active” code and data is actually in memory
    Allocate more memory to process as needed
Provide protection
  One process can’t interfere with another
    Because they operate in different address spaces
  User process cannot access privileged information
    Different sections of address space have different permissions
B.4 Virtual Memory

## Slide 7: A Simplified View of Virtual Memory
CPU
0:
1:
N-1:
Memory
0:
1:
P-1:
Page Table
Virtual
Addresses
Physical
Addresses
Disk
B.4 Virtual Memory
Notes: page/segment is the base unit of data transferred between memory and disk

## Slide 8: Cache vs Virtual Memory
B.4 Virtual Memory
Notes: Note that miss penalty of VM is much larger than that of cache.
Note that in virtual memory, access time is much higher than transfer time

## Slide 9: Cache vs Virtual Memory
Terminology
  Block  page
  Cache miss  page fault
Replacement on cache memory misses by hardware whereas virtual memory replacement is by OS
Size of processor address determines size of VM whereas cache size is independent of address size
VM can have fixed or variable size blocks
  page vs segmentation: they both have pros and cons
B.4 Virtual Memory

## Slide 10: Virtual Memory Design Issues
Page size should be large enough to try to amortize high access time of disk
  Typical size: 4KB – 16KB
Reducing page fault rate is important
  Fully associative placement of pages in memory
Page faults not handled by hardware
  OS can afford to use clever algorithm for page replacement to reduce page fault rate
Write-through approach is too expensive
  Write back approach is always used
B.4 Virtual Memory
Notes: note that disk access time is much higher than transfer time -> large page size.
But large page size can lead to waste of memory.

## Slide 11: Virtual Memory Address Translation
virtual page number
page offset
virtual address
[n-1..0]
physical page number
page offset
physical address
[m-1..0]
0
p–1
p
m–1
n–1
0
p–1
p
Address Translation
From CPU
To memory
B.4 Virtual Memory
Notes: size of page offset is determined by page size

## Slide 12: Address Translation
virtual page number (VPN)
page offset
virtual address
physical page number (PPN)
page offset
physical address
0
p–1
p
m–1
n–1
0
p–1
p
page table base register
if valid=0 then page is not in memory
valid
physical page number (PPN)
access
Each process has its own page table.
B.4 Virtual Memory

## Slide 13: Address Translation - Example
1010 1111 1101 1100
1111 1111 1010 1000
…
…
…
1111 1010 1111
…
0
1111 1111 1111 1111
1111 1010 1111
1010 1111 1101 1100
Physical Address:
0xFFFF87F8
Page Table base register
Page Offset
Virtual Page Number
Physical Page Number
Page Offset
B.4 Virtual Memory
page table

## Slide 14
Review the cache optimization
Avoid Address Translation during Cache Indexing to Reduce Hit Time

## Slide 15: Page Faults
What if object is on disk rather than in memory?
  Page table entry indicates virtual address not in memory
  OS exception handler invoked to move data from disk into memory
  Current process suspends, others can resume
    OS has full control over placement, etc.
CPU
Memory
Page Table
Disk
Virtual
Addresses
Physical
Addresses
CPU
Memory
Page Table
Disk
Virtual
Addresses
Physical
Addresses
Before fault
After fault
B.4 Virtual Memory

## Slide 16: Servicing Page Faults
Processor signals controller
  Read block of length P starting at disk address X and store starting at memory address Y
Read occurs
  Direct Memory Access (DMA)
  Under control of I/O controller
I/O controller signals completion
  Interrupt processor
  OS resumes suspended process
disk
Disk
disk
Disk
Memory-I/O bus
Processor
Cache
Memory
I/O
controller
Reg
(2) DMA Transfer
(1) Initiate Block Read
(3) Read Done
B.4 Virtual Memory
Notes: More on this in OS course.

## Slide 17: Page Replacement
When there are no available free pages to handle a fault, we must find a page to replace.
This is determined by the page replacement algorithm.
The goal of the replacement algorithm is to reduce the fault rate by selecting the best victim page to remove.
  Again, due to high access latency to disk
LRU is the most popular replacement policy.
  Each page is associated with a use/reference bit.
  It is set whenever a page is accessed.
  OS periodically clears these bits.
  Pages with the use bit reset are candidates for replacement
B.4 Virtual Memory

## Slide 18: Fast Address Translation – TLB
tags from VAs
Physical page number
B.4 Virtual Memory
Notes: Virtually addressed physically tagged L1 cache – parallel TLB and L1 access.
Explain what happens on TLB misses, L1/L2 misses.

## Slide 19: TLB in AMD Opteron
B.4 Virtual Memory
Figure B.24 Operation of the Opteron data TLB during address translation. The four steps of a TLB hit are shown as circled numbers. This TLB has 40 entries. Section B.5 describes the various protection and access fields of an Opteron page table entry.
Notes: this TLB is fully associative

## Slide 20: Question: Page size and Page Table Size
Assume 32-bit virtual address
  Page table size if page size is 4K?
  Page table size if page size is 16K?
What about 64-bit virtual address?
B.4 Virtual Memory

## Slide 21: Multi-Level Page Table
Higher level PTEs point to lower level tables
PTEs at bottom level hold PPN
Different parts of VAs used to index tables at different levels
Virtual address
Notes: # of levels of page table hierarchy depends on the size of virtual addresses

## Slide 22: Multi-Level Page Table
Large VA space is unused
If a entry in level L is null, the tables at lower levels (those to the right) are not stored in memory
Virtual address

## Slide 23: Selecting Page Size – Large Page Size
Smaller page table
  A page table can occupy a lot of space
Larger L1 cache
Less TLB misses, faster translation
More efficient to transfer larger pages from 2nd storage
Wasted memory usage
Wasted IO bandwidth
Slower process start up
B.4 Virtual Memory

## Slide 24: Virtual Memory – Protection
Virtual memory and multiprogramming
  Multiple processes sharing processor and physical memory
Protection via virtual memory
  Keeps processes in their own memory space
  only OS can update page tables
Role of architecture:
  Provide user mode and supervisor mode
  Protect certain aspects of CPU state: PC, register, etc
  Provide mechanisms for switching between user mode and supervisor mode
  Provide mechanisms to limit memory accesses
  Provide TLB to translate addresses
B.5 Protection of Virtual Memory

## Slide 25: Page Table Entries – Protection
Address – physical page number
Valid/present bit
Modified/dirty bit
Reference bit
  For LRU
  Protection bits – Access right field defining allowable accesses
    R/W/X: read only, read-write, execute only
    User/Supervisor

## Slide 26: Page Table Entries – Protection
Check bits on each access and during a page fault
  If violated, generate exception (Access Protection exception)

## Slide 27: Summary
OS virtualizes memory and IO devices
  Each process has an illusion of private CPU and memory
Virtual memory
  Arbitrarily large memory, isolation/protection, inter-process communication
  Reduce page table size
  Translation buffers – cache for page table
  Manage TLB misses and page faults
  Protection